## Safety Guidelines for Quinzhee Construction

Warning! Read the safety guidelines for this activity before attempting construction of a Quinzhee. This activity is not appropriate for unsupervised students and requires at least 2 adults willing to do vigorous physical work. A simpler alternative is provided at the end of this article.

  - Do not attempt to build quinzhees larger than the 3 or 4 person structure described in the accompanying Building a Quinzhee document without the help of someone who has significant experience with snow shelters. Suffocation can occur rapidly if you are buried under the snow.

  - Wear layers of clothing instead of a single heavy snow suit so that you can take off and add layers according to how hard you are working and how the air temperature fluctuates. Have a warm and dry set of clothing set aside for when you are done along with a thermos of hot cocoa or tea.

  - Avoid using large shovels. More small shovels full of snow will reduce the chances of back injuries.

  - Pack the perimeter of the shelter well and make the snow pile a dome shape. A peak on the outside could cause the shelter to collapse.

  - Let the snow pile firm up before starting to hollow out the quinzhee. An hour is often sufficient. If you hear a “whoomph” while you are digging out the shelter, get out immediately, let it settle another hour and try again.

  - Always dig out a quinzhee with a partner standing outside the door with a shovel. The “doorman” will remove snow you shovel out and, more importantly, can dig you out if the snow collapses. Quinzhees are weakest during construction.

  - A dome shape is important on the inside as well as the outside. Flat ceilings collapse more easily.

  - The person digging out the inside will get wet. Be prepared with dry clothes and a hot drink when the person comes out.

  - Sleep on an insulated and waterproof sleeping pad under a good winter rated sleeping bag. Remember, the temperature in the quinzhee may be significantly warmer than outside but it won’t be above freezing – you hope!

  - Always have a shovel inside the quinzhee with you. It is so quiet inside that you won’t even hear the storm that plugs your doorway with snow!