## Slide 1: Mood Ring Project Basics
for TI-84 Plus CE

## Slide 2: Digital Mood Ring (introduction to STEM and coding Projects for all levels)
Project Summary:
Bring science and coding together (no coding experience necessary) while developing a mood ring! Explore the science of color mixing while determining the right body temperature thresholds.
This is an excellent first TI-Innovator STEM and coding project. The project includes variables, loops, conditional statements, Boolean operators and other fundamental programming concepts.
Students will complete a series of smaller challenges, as they build the skills needed to complete the final challenge!

## Slide 3: Digital Mood Ring Challenges:
Challenge 1: Use SET COLOR to explore using the color LED. Try to find the RGB values of all the colors in the mood chart.
Challenge 2: Use DispAt command to display your name at several locations on the screen.
Challenge 3: Use a For..EndFor loop to display the numbers 1 through 10.
Challenge 4: Connect a temperature sensor to the TI-Innovator Hub and display the temperature on the calculator.
Challenge 5: Use a loop to read and display temperature.
Challenge 5 Extension (Optional): Use a loop to read, display and log into list arrays for time and temperature. Graph the result.
Challenge 6: Use a While..EndWhile loop along with getKey() command to monitor temperature and make a decision to display a message, “Hot” or “Cold”. Then modify your program to include a 3rd level between hot and cold, “Nice”.
Final Challenge: Build a mood ring to repeatedly read the temperature sensor, determine the mood of the person, display the temperature value and display the mood.

## Slide 4: TI-84 Plus CE Resources:
Step-by-Step YouTubevideos designed for the teacher with a detailed, demonstration of each challenge.
  **The videos are intended to guide those new programming in general, programming on the TI-84 Plus CE and programming with the TI-Innovator Hub.
  https://www.youtube.com/playlist?list=PL17Fe0ZmhCR-PAuv5pw85vxrtLu5YGeWl
10 Minutes of Code with TI-Innovator:
  https://education.ti.com/en/activities/ti-codes/84/10-minutes-innovator
10 Minutes of Code Teacher’s Lounge (TI-84 Plus CE): Select link to download zip files with PDF’s of all of the 10 Minutes of code lessons, teacher and student documents.
  https://education.ti.com/en/activities/ti-codes/84/teacher-lounge
TI-Innovator Technology eGuide
  https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html
TI-Innovator Hub Commands
  https://education.ti.com/html/webhelp/EG_Innovator/EN/content/eg_innovsys/resources/pdf/ti-innovator_hub_commands_en.pdf
TI-84 Plus CE TI-Basic Programming Guide
  https://education.ti.com/html/webhelp/EG_TI84PlusCECode/EN/index.html
TI-84 Plus CE Reference Guide
  https://education.ti.com/html/webhelp/EG_TI84PlusCECode/EN/index.html

## Slide 5: Background: Input/Output Commands for Displaying and Requesting text strings and numeric values
Display a string
Display a numeric value
Request a numeric value input
Row
Variable for the input numeric value
Clear the screen
Program I/O
Column
Display

## Slide 6: Background: For Loop
Control variable
Ending Value
Program Control Menu (CTL)
Initial Value

## Slide 7: Background: Decision Making and Logic Statements
If-Then command
If-Then-Else command
“and”
“or”
Logic functions
Decision Making Commands
Note: Relational and Logic operators can be found on the keyboard using 2nd Math.

## Slide 8: Background: While…EndWhile loop
The While loop repeats a set of commands as long as the While condition is true.
Command Syntax:
While condition
Commands in While block
EndWhile
Note: This program uses the BRIGHTNESS sensor as a control for the While loop. If you completely cover the sensor the While loop will stop.

## Slide 9: Background: Advanced Version Storing Data in an Array
Declare an array variable
Inside a loop store a calculation or Store a value from a sensor
Values can be plotted or used in other calculations.

## Slide 10: Background: Advanced Version Ending a loop using a keypress
Initialize default value.
Continually set the value of keys pressed.
This example exits
0 →K
While K≠45
getKey →K
“ set of commands executed while clear key isn’t pressed
End

## Slide 11: Background: Basics of programming with the TI-84 CE.

## Slide 12: Create a new program
Press [Prgm] key
Select New and give it a name

## Slide 13: Code Program

## Slide 14: Execute your program
1. [2nd] [quit]
2. Select the program
3. Press [enter]

## Slide 15: Completed Project CODE:

## Slide 16: Background: Example Program (Basic)
Send(“CONNECT TEMPERATURE 1 TO IN 1”)
Wait 0.5
ClrHome
Output(1,1,”THE MOOD RING”)
Output(8,1, “HIT CLEAR TO QUIT”)
For(A,1,30)
Send(“READ TEMPERATURE 1”)
Get(T)
Output(4,1,”TEMPERATURE (°C) = “)
Output(4,18,T)
If T<24
Then
Send(“SET COLOR 0 0 0”) Output(5,1,”YOU ARE STRESSED”)
END
If T≥24 and T<26
Then
Send(“SET COLOR 255 0 0”) Output(5,1,”YOU ARE NERVOUS”)
END
If T≥26
Then
Send(“SET COLOR 0 255 0”) Output(5,1,”YOU ARE ACTIVE”)
END
Wait 0.5
END
Send(“SET COLOR 0 0 0”)
Additional Challenges
Add more than three moods.
Replace the For loop with a While loop that allows the user to stop the sampling process.
Note: Experiment with temperature values to determine relevant temperature ranges for each person.

## Slide 17: Background: Example Program (Advanced)
1→A
0 →T
0 →S
0 →F
0 →K
1 →N
0 →dim(L1)
0 →dim(L2)
Send(“CONNECT TEMPERATURE 1 TO IN 1”)
Wait 0.5
ClrHome
Output(1,1,”THE MOOD RING”)
Output(8,1, “HIT CLEAR TO QUIT”)
For(A, 1, 10) Send(“READ TEMPERATURE 1”)
Get(T)
T+S →S
Wait 0.1
End
S/10 →F
While K≠45
getKey →K
Send(“READ TEMPERATURE 1”)
Get(T)
Output(4,1,”TEMPERATURE (°C) = “)
Output(4,18,T)
If T<F+1
Then
Send(“SET COLOR 0 0 0”) Output(5,1,”YOU ARE STRESSED”)
END
Additional Code
Stores the temperature values and the time to list variables. This data can be displayed on a plot of time vs. temperature after the loop is done.
For loop was replaced with a While loop that allows the user to stop the sampling process.
If T≥F+1 and T<F+2
Then
Send(“SET COLOR 255 0 0”) Output(5,1,”YOU ARE NERVOUS”)
END
If T≥F+2 and T<F+3
Then
Send(“SET COLOR 255 150 150”) Output(5,1,”YOU ARE USETTLED”)
END
If T≥F+3 and T<F+4
Then
Send(“SET COLOR 0 255 0”) Output(5,1,”YOU ARE ACTIVE”)
END
If T ≥ F+4
Then
Send(“SET COLOR 0 255 150”) Output(5,1,”YOU ARE RELAXED”)
END
Wait 0.5
N*0.5 →L1(N)
T →L2(N)
N+1 →N END
Send(“SET COLOR 0 0 0”)