Objective: Compare the slopes of a secant line and the tangent line at point P. In this activity, you will graph y1(x)=x2 and find the slopes. If point P(1, 1) and point Q are two points on y1(x) that define a secant line, then the slope of the secant line is , where x is the x-coordinate of point Q.

Problem 1 – Graphing secant and tangent Lines

Step 1: Press ( ( to go to the Y= screen. At y1, press ( ( (. Step 2: Press ( (. Set the window to –3.5 to 3.5 for the x-axis and –10 to 10 for the y-axis. Use xscl and yscl of 1 to have tick marks show every unit. Step 3: Press ( ( to graph. Step 4: To draw the tangent line to y=x2 at (1, 1), press ( and arrow down to select Tangent. When prompted with the question Tangent at? Press ( (. Record the equation of the tangent line at (1, 1). ___________________ What is the slope of the line? __________________ Step 5: Return to the Y= screen. In y2(x) graph a secant line that passes through point P(1, 1) and point Q(3, 9). What is the slope of this line? _____________ Begin with the point-slope form of an equation. Show the work to explain why you should graph y2(x) = 4(x – 1) + 1. What could be done to bring point Q closer to point P(1, 1)? What value does the slope need to approach?

Step 5: On the Y= screen, change the slope of the secant line to 3.5. Observe the graph. Then change the slope to 3 and observe the graph. Note the intersection points P and Q. Repeat one more time, making the slope of the secant line 2.5. As point Q approaches point P, what do you notice about the secant and tangent lines?

Problem 2 – Finding average rate of change

Step 6: Turn y2(x) off by pressing ( when the cursor is next to y2(x) on the Y= screen. Step 7: Press ( ( to set up the table to analyze the function numerically. Change tblStart to 1 and (tbl to 0.1. Step 8: Press ( ( to see the x- and y-coordinates of y1(x)=x2. The average rate of change of function on an interval [a, b] is the slope of the secant line containing and Use the table of values of to find the average rate of change of y1(x) on the interval [1, 1.1]. Show what you inputted into the calculator (().

Problem 3 – Finding instantaneous rate of change

The instantaneous rate of a change of a function at a given point is the slope of the tangent line to the function at that point. If the tangent line is not known, then the secant line slope can be used as an approximation. The calculation from Problem 2 is an example of such an approximation. How can you find an even better estimate of the instantaneous rate of change of y1(x) at x = 1? Use the calculator to find a better estimate of the instantaneous rate of change of y1(x) at x = 1. Show what you inputted into the calculator.

Extension – Rectilinear Motion Application Use your calculator to answer the following questions. For each answer, be sure to include appropriate units. Suppose a particle is traveling along a horizontal line such that its position is given by the function where is measured in meters and is measured in seconds. 1. What is the average rate of change of the position function from t = 2 to t = 4? 2. Estimate the instantaneous rate of change of the position function at t = 2? The velocity of the particle is given by the function where v is measured in meters per second and t is measured in seconds. 3. What is the average rate of change of the velocity function from t = 2 to t = 4? 4. Estimate the instantaneous rate of change of the velocity function at t = 2?