## Slide 1: Mood Ring STEM/STEAM Event Handout
TI-84 Plus CE

## Slide 2
Digital Mood Ring Program for TI-84 Plus CE
PROGRAM: MOODEVNT
Send ("CONNECT TEMPERATURE 1 TO IN1”)
ClrHome
Output(1,1,”THE MOOD RING”)
Output(8,1,”PRESS CLEAR TO QUIT”)
0→K
While K≠45
getKey →K
Send("READ TEMPERATURE 1”)
Get T
Output(4,1,"TEMPERATURE(°C)= ”)
Output(4,18,T)
If T<24
Then
Send("SET COLOR 255 0 0”)
Output(5,1,”YOU ARE STRESSED ”)
End
If T≥24 and T<26
Then
Send("SET COLOR 255 100 175”)
Output(5,1"YOU ARE HAPPY ”)
End
If T≥26
Then
Send("SET COLOR 0 255 150”)
Output(5,1,"YOU ARE RELAXED “)
End
Wait 0.5
End
Send("SET COLOR 0 0 0”)
While Loop
Set-up
Wrap-up
Read, Get, Store
Temp values to variable t and Display t
Use logic to check values of variable T.
Determine Mood and Color.
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.

## Slide 3
Digital Mood Ring Program for TI-84 Plus CE
PROGRAM: MOODEVNT
Send ("CONNECT TEMPERATURE 1 TO IN1”)
ClrHome
Output(1,1,”THE MOOD RING”)
Output(8,1,”PRESS CLEAR TO QUIT”)
0→K
While K≠45
getKey →K
Send("READ TEMPERATURE 1”)
Get T
Output(4,1,"TEMPERATURE(°C)= ”)
Output(4,18,T)
If T<24
Then
Send("SET COLOR 255 0 0”)
Output(5,1,”YOU ARE STRESSED ”)
End
If T≥24 and T<26
Then
Send("SET COLOR 255 100 175”)
Output(5,1"YOU ARE HAPPY ”)
End
If T≥26
Then
Send("SET COLOR 0 255 150”)
Output(5,1,"YOU ARE RELAXED ”)
End
Wait 0.5
End
Send("SET COLOR 0 0 0”)
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.
Edit the program to make it your own.

## Slide 4: Mood Ring STEM/STEAM Event Handout – Halloween Edition
TI-84 Plus CE

## Slide 5
Digital Mood Ring Program for TI-84 Plus CE
PROGRAM: MOODEVNT
Send ("CONNECT TEMPERATURE 1 TO IN1”)
ClrHome
Output(1,1,”THE MOOD RING”)
Output(2,1,”HALLOWEEN EDITION”)
Output(8,1,”PRESS CLEAR TO QUIT”)
0→K
While K≠45
getKey →K
Send("READ TEMPERATURE 1”)
Get T
Output(4,1,"TEMPERATURE(°C)= ”)
Output(4,18,T)
If T<24
Then
Send("SET COLOR 255 0 0”)
Output(5,1,”YOU ARE A ZOMBIE ”)
End
If T≥24 and T<26
Then
Send("SET COLOR 255 100 175”)
Output(5,1"YOU ARE A VAMPIRE”)
End
If T≥26
Then
Send("SET COLOR 0 255 150”)
Output(5,1,"YOU ARE A MUMMY “)
End
Wait 0.5
End
Send("SET COLOR 0 0 0”)
While Loop
Set-up
Wrap-up
Read, Get, Store
Temp values to variable t and Display t
Use logic to check values of variable T.
Determine Mood and Color.
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.

## Slide 6
Digital Mood Ring Program for TI-84 Plus CE
PROGRAM: MOODEVNT
Send ("CONNECT TEMPERATURE 1 TO IN1”)
ClrHome
Output(1,1,”THE MOOD RING”)
Output(2,1,”HALLOWEEN EDITION”)
Output(8,1,”PRESS CLEAR TO QUIT”)
0→K
While K≠45
getKey →K
Send("READ TEMPERATURE 1”)
Get T
Output(4,1,"TEMPERATURE(°C)= ”)
Output(4,18,T)
If T<24
Then
Send("SET COLOR 255 0 0”)
Output(5,1,”YOU ARE A ZOMBIE ”)
End
If T≥24 and T<26
Then
Send("SET COLOR 255 100 175”)
Output(5,1"YOU ARE A VAMPIRE”)
End
If T≥26
Then
Send("SET COLOR 0 255 150”)
Output(5,1,"YOU ARE A MUMMY “)
End
Wait 0.5
End
Send("SET COLOR 0 0 0”)
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.
Edit the program to make it your own.