| Overview: | AP Computer Sceience Principles Computational Thinking Practices: |
| --- | --- |
| Build a flippy do and slip it over your TI-RGB Array to explore base two numbers using the manipulatieve. Write a TI-BASIC program to abstract a representation of a decimal number in a binary format on the TI-RGB Array. | LO 2.1.1 – Describe the variety of abastractions used to represent data. LO 2.1.2 – Explain how binary sequences are used to represent digital data. LO 2.2.1 – Develop an abstraction when writing a program or creating other computational artifacts. |
| The TI-RGB Array can be used as a binary display. Notice the numbering of the pixels is in place value order. A pixel that is on represents the digit 1 while off represents the digit 0. | An example of the decimal number 13 displayed on the TI_RGB Array with the coresponding calculation. 1x23+1x22+0x21+1x20=13 |
| Directions: |
| Follow the instructions on the printout to Build you Flippy-Do. Slide the Flippy-Do on the TI-RGB Array. Fold the tabs up or down to match the binary number in the table. Fill in in the remainder of the table on the right. Do you see a pattern? | Decimal 4–bit binary number Pixel 3 Pixel 2 Pixel 1 Pixel 0 0 0000 off off off off 1 0001 off off off on red 2 0010 off off on red off 3 0011 off off on red on red 4 5 6 7 8 9 |
|  | Decimal 4–bit binary number Pixel 3 Pixel 2 Pixel 1 Pixel 0 10 11 12 13 14 15 |
| The table to the right contains every 8-bit number that has a single 1 in it. Do you notice a pattern? Fill out the remainder of the table writeing down the power of two and the decimal equivalent next to each binary number. | Decimal 8-bit binary number Power of 2 1 0000 0001 20 2 0000 0010 21 4 0000 0100 23 0000 1000 0001 0000 0010 0000 0100 0000 1000 0000 |
| Challenge 3: Write a program to turn on the TI_RGB Array for the number 13 and display the calculated decimal value as the sum of powers of 23 through 20. Set the tabs of the Flippy-Do up or down for the number 13. Run the program. Do the pixels on the TI_RGB Array match the number on the Flippy-Do? Modify your program to match a few more numbers from the table. Do you see how the TI_RGB Array can display binary numbers? Challenge 3 Optional Extension: Try to represent the decimal 170 as an eight bit binary number. | Define c2()= Prgm Send "CONNECT RGB " Send "SET RGB 0 255 0 0" Send "SET RGB 1 0 0 0" Send "SET RGB 2 255 0 0" Send "SET RGB 3 255 0 0" decimal:=1*23 + 1*22 +0*21 + 1*20 Disp "Decimal = ",decimal EndPrgm |