## Slide 1: Mood Ring STEM/STEAM Event Handout
TI-Nspire

## Slide 2
Digital Mood Ring Program for TI-Nspire
Define moodevent()=
Prgm
Send "CONNECT TEMPERATURE 1 TO IN1"
key=" ”
DispAt 1,”Digital Mood Ring"
DispAt 8,"Press esc key to quit"
While key≠"esc"
key=getKey()
Send "READ TEMPERATURE 1"
Get t
DispAt 4,"Temperature =",t,"°C"
If t<24 Then
Send "SET COLOR 255 0 0"
DispAt 5,"You are STRESSED"
EndIf
If t≥24 and t<26 Then
Send "SET COLOR 255 100 175"
DispAt 5,"You are HAPPY"
EndIf
If t≥26 Then
Send "SET COLOR 0 255 150"
DispAt 5,"You are RELAXED "
EndIf
Wait 0.5
EndWhile
Send "SET COLOR 0 0 0"
EndPrgm
While Loop
Set-up
Wrap-up
Read, Get, Store
Temp values to variable t and Display t
Use logic to check values of variable t.
Determine Mood and Color.
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.

## Slide 3
Digital Mood Ring Program for TI-Nspire
Define moodevent()=
Prgm
Send "CONNECT TEMPERATURE 1 TO IN1"
key=" ”
DispAt 1,”Digital Mood Ring"
DispAt 8,"Press esc key to quit"
While key≠"esc"
key=getKey()
Send "READ TEMPERATURE 1"
Get t
DispAt 4,"Temperature =",t,"°C"
If t<24 Then
Send "SET COLOR 255 0 0"
DispAt 5,"You are STRESSED"
EndIf
If t≥24 and t<26 Then
Send "SET COLOR 255 100 175"
DispAt 5,"You are HAPPY"
EndIf
If t≥26 Then
Send "SET COLOR 0 255 150"
DispAt 5,"You are RELAXED "
EndIf
Wait 0.5
EndWhile
Send "SET COLOR 0 0 0"
EndPrgm
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.
Edit the program to make it your own.

## Slide 4: Mood Ring STEM/STEAM Event Handout – Halloween Edition
TI-Nspire

## Slide 5
Digital Mood Ring Program for TI-Nspire
Define mood1031()=
Prgm
Send "CONNECT TEMPERATURE 1 TO IN1"
key=" ”
DispAt 1,”Digital Mood Ring”
DispAt 2,”Halloween Edition"
DispAt 8,"Press esc key to quit"
While key≠"esc"
key=getKey()
Send "READ TEMPERATURE 1"
Get t
DispAt 4,"Temperature =",t,"°C"
If t<24 Then
Send "SET COLOR 50 120 255"
DispAt 5,"You are a Zombie"
EndIf
If t≥24 and t<26 Then
Send "SET COLOR 255 0 0"
DispAt 5,"You are a Vampire"
EndIf
If t≥26 Then
Send "SET COLOR 160 42 42"
DispAt 5,"You are a Mummy "
EndIf
Wait 0.5
EndWhile
Send "SET COLOR 0 0 0"
EndPrgm
While Loop
Set-up
Wrap-up
Read, Get, Store
Temp values to variable t and Display t
Use logic to check values of variable t.
Determine Mood and Color.
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.

## Slide 6
Digital Mood Ring Program for TI-Nspire
Define mood1031()=
Prgm
Send "CONNECT TEMPERATURE 1 TO IN1"
key=" ”
DispAt 1,”Digital Mood Ring”
DispAt 2,”Halloween Edition"
DispAt 8,"Press esc key to quit"
While key≠"esc"
key=getKey()
Send "READ TEMPERATURE 1"
Get t
DispAt 4,"Temperature =",t,"°C"
If t<24 Then
Send "SET COLOR 50 120 255"
DispAt 5,"You are a Zombie"
EndIf
If t≥24 and t<26 Then
Send "SET COLOR 255 0 0"
DispAt 5,"You are a Vampire"
EndIf
If t≥26 Then
Send "SET COLOR 160 42 42"
DispAt 5,"You are a Mummy "
EndIf
Wait 0.5
EndWhile
Send "SET COLOR 0 0 0"
EndPrgm
Change mood by editing text.
Change colors by editing values,
0 to 255, of RED GREEN BLUE.
Change temperature ranges by editing
threshold values.
Edit the program to make it your own.